## Slide 1: Elliptic Curve Cryptography
Palmer Dabbelt and Kevin Linger

## Slide 2: Public-Key Cryptography
Solve key distribution problem
  Public key and private key
Based on asymmetric mathematics
  Solving the discrete logarithm problem
Widely used
  SSL/TLS, SSH, …

## Slide 3: Why Elliptic Curves?
We could use many groups
Probably-prime finite integers
  Fast in HW, sub-exp algorithms known
Elliptic Curves
  Slow in HW, no sub-exp algorithms known
Security | Integer | EC | Ratio
80 | 1024 | 160 | 3:1
112 | 2048 | 224 | 6:1
128 | 3072 | 256 | 10:1
192 | 7680 | 384 | 32:1
256 | 15360 | 521 | 64:1

## Slide 4: What is an Elliptic Curve?
EC on real numbers
Some constants
Closed under addition
More expensive
Need a finite field

## Slide 5: Design Space
ALU structure
  Large multiplier vs. chained small multipliers
  Specific hardware units vs. general purpose
Complexity of control block
  Could have some state managed by Rocket
Changing the algorithm
  Already been done, probably just pick one

## Slide 6: ALU Structure
Many different ALU functions performed
  Squaring, multiplication, and more
  Introduces knobs for design-space exploration

## Slide 7: Rocket Interface
Instructions: Sign, Validate
  Introduce more instructions with control block
  Include information about key size
Memory accesses are very limited
  One load, lots of compute, one store
  Storage vs. moving data through 64-bit pipe
Synchronous or asynchronous interface?