## Slide 1
Rocket coprocessor for accelerating elliptic curve cryptography (specifically, ECDSA)
Elliptic Curve Accelerator
Results
Discrete Logarithm
Why ECDSA?
Elliptic Curves
Public-Key Cryptography
Two keys, called a keypair
  Public: the whole world can know this
  Private: only the owner knows this
Four operations
  Sign(Message, Private) → Signature
  Verify(Message, Signature, Public) → Boolean
  Encrypt(Message, Public) → Cyphertext
  Decrypt(Cyphertext, Private) → Message
ECDSA is a widely-used signature algorithm
  Supports Sign() and Verify()
Kevin Linger, Palmer Dabbelt
ECDSA
Accelerator Core
Elliptic curve: the set of points that satisfy
Some crypto-specific constraints
  Finite field -> everything is modular
  Difficult -> modulo some large number
  Difficult in one direction (given and find )
  Easy in the other direction (given and find )
Basis for many public-key crypto algorithms
Full RTL in Chisel
  Primetime for power numbers
  Simulation for performance numbers
Two common fields for public-key crypto
  : Integers modulo a prime, repeating multiplication
  : Elliptic curves modulo a prime, repeating addition
Integer fields have a sub-exponential reversal
HW/SW Co-tuning
ECDSA consists of many operations
  Each can be implemented in HW or SW
  Which operations deserve die space?
Configurable C++ ECDSA code
  Capable of running all in software
  Operations can be selection for hardware
Generate matching C++ and RTL
  Easy thanks to Chisel!
Notes: Please put in notes here to explain poster so that someone else could summarize what your poster is about