## Slide 1
Elliptic Curve Crypto Accelerator Kevin Linger & Palmer Dabbelt, UC Berkeley
The Ubiquitous Swarm Lab at UC Berkeley
Your picture here
Your photo here
Motivation
Why ECDSA?
Two common fields for public-key crypto
  : Integers modulo a prime, repeating multiplication
  : Elliptic curves modulo a prime, repeating addition
Integer fields have a sub-exponential reversal
Smaller key sizes are great for embedded systems
  Comparison of key sizes needed for elliptic curves vs integer fields
Results
  Results of various hardware configurations using 32 nm educational libraries
HW/SW Co-tuning
ECDSA consists of many operations
  Each can be implemented in HW or SW
  Which operations deserve die space?
Configurable C++ ECDSA code
  Capable of running all in software
  Operations can be selected for hardware
Generate matching C++ and RTL
  The Chisel project at Berkeley makes this easy!
Ellpitic Curves
Ellptic Curve Arithmetic
Public Key Crypto relies on the discrete logarithm problem
  Easy to go one direction but not the other
  In ECDSA, the discrete log is an elliptic curve point multiply
  G*d = P, where G and P are points and d is the private key
Point Multiply is repeated point addition
  Defined geometrically, see figure
  Takes exponential time unless the multiplier is known
  Geometric representation of an elliptic curve and a point addition
  Integer operations need for a point addition. When repeated becomes a multiply.
Original motivating project: Universal Dataplane
  Large number of nodes (10^15)
  Low power per node (µW)
Designed with security in mind
  Encrypt and sign every transmission
  Unique key-pair for every node (hard with RSA!)
On a CPU, ECDSA is mJ per signature
  1 transmission per 1000 seconds burns the budget!
  We need a 1000x improvement in energy per signature
Swarm devices have limited capabilities
  What is the bare amount of hardware needed?
  Is specialized hardware for crypto worth it?
  Components of the Universal Dataplane
Elliptic curve: the set of points that satisfy
  y^2 = x^3 + ax + b
Some crypto-specific constraints
  Finite field -> everything is modular
  Difficult -> modulo some large number